## Slide 1: COMP130177.01 互联网体系结构 2. 挑战和技术路线
赵进
School of
School of Computer Science, Fudan University

## Slide 2: Review on last week
What is architecture:
  At a very abstract level, the architecture of a system defines how the system is broken into parts and how those parts interact.
Modularity and abstraction are central tenets of Computer Science thinking.
  模块化 Modularity breaks a system into parts, normally to permit independent construction and replacement, reuse of parts, and so on.
  抽象 Abstraction is a refinement of modularity—it is the gathering together of some complex mechanism into a module, and providing a simple interface by which this complexity is hidden.

## Slide 3: Layering
Selecting and specifying good module boundaries is an art.
A popular and simple structure is a layered model: lower layer mechanisms provide interfaces to their functions, which are then used by higher-level functions.
Why layering?
  Dependency：how each module depends on the correct operation of others.
  Mutual dependency is known to be complex, and this leads to the desire for a loop-free dependency graph, which implies layers.

## Slide 4: Layering: End-to-End
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame
SONET frame

## Slide 5: Today’s talk
面临挑战
“革命型” 、“演进型” 路线

## Slide 6: The Internet: A Remarkable Story
Tremendous success
  From research experiment to global infrastructure
Brilliance of under-specifying
  Network: best-effort packet delivery
  Programmable hosts: arbitrary applications
Enables innovation
  Apps: Web, P2P, VoIP, social networks, …
  Links: Ethernet, fiber optics, WiFi, cellular, …

## Slide 7: A History of Internet Evolution
Hard to change IP
  …especially after 1990
IP
Applications
Technology
Innovation both above and below IP

## Slide 8: 互联网的发展
经过 50 年的不断发展、应用和完善，Internet 从最初的单一军用网络不断在向包括军用、民用、商用等的各个方面普及
互联网的核心是TCP/IP协议栈
  传统 TCP/IP 网络设计目的是进行可靠的数据传输，因此
  IP 协议是一种无连接的、基于数据报文的传输模式， 提供“尽力而为”的服务
  TCP 使用的重传和滑动窗口机制给实时数据的传输带来难以预料的时间延迟以及抖动，无法保证吞吐量和传送时延等服务质量 （QoS）要求。

## Slide 9: 面临的挑战
随着网络用户的不断增多，网络规模不断扩大，网络承载了多种多样的新型业务，呈现出了不断变化的需求，传统网络无法很好地满足这些新业务和新需求， 并逐渐暴露出一系列问题。
导致现有互联网正面临着前所未有的挑战，包括
  可扩展性、安全性、管控性、移动性、 服务分发能力、绿色节能等一系列问题。
为什么会这样 ？
  体系结构的问题

## Slide 10: 回顾互联网体系结构的设计目标
Fundamental Goal：（Connect existing networks）
  The top level goal for the DARPA Internet Architecture was to develop an effective technique for multiplexed utilization of existing interconnected networks.
  The components of the Internet were networks, which were to be interconnected to provide some larger service.
  The technique selected for multiplexing was packet switching.
    why not circuit switching? (statistical utilization, simple IP layer abstract )

## Slide 11: Network of Networks
Roughly hierarchical
at center: “tier-1” ISPs (e.g., UUNet, BBN/Genuity, Sprint, AT&T), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately

## Slide 12: Decisions
Packet switching as basis for multiplexing
Store-and-forward gateways as basis for interconnection
“Fate-sharing” model for reliability
Layering
Minimal assumption about the network

## Slide 13: Packet switching
Basic Philosophy
  Divide data into packets
  Packets travel separately
  Enables statistical multiplexing
Best-effort delivery
  Packets may be lost, delayed, out-of-order
  Simplify network design and failure handling
  Build timely, ordered, reliability delivery on top

## Slide 14: Packet switching
Invented by Baran, Kleinrock et al. in early 60s
Radical departure from circuit switched model
Far more efficient for data communication since it is bursty (peak >> average)
Key idea: statistical multiplexing
  – share on demand
  – based on statistics of offered load rather than a fixed offered load

## Slide 15: Statistical Multiplexing: Example
One user sends at 1 Mbps and is 90% idle
  10 Mbps channel: 10 users if statically allocated,
  1 Mbps channel if perfect multiplexing
Occasional oversubscription
  need for buffering inside the network – need for loss recovery
  need for congestion control

## Slide 16: Interconnection
Hide underlying technology from applications
Decisions:
  Network provides minimal functionality
  “Narrow waist”
Tradeoff: No assumptions, no guarantees.
Technology
Applications
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...

## Slide 17: The “Curse of the Narrow Waist”
IP over anything, anything over IP
  Has allowed for much innovation both above and below the IP layer of the stack
  An IP stack gets a device on the Internet
Drawback: very difficult to make changes to IP
  But…people are trying
  Many proposals to
    US: NSF GENI project: http://www.geni.net/
    EU: FIRE(Future Internet Research and Experimentation)
    China: Many future network initivatives

## Slide 18: Second Level Goals
survivability in the face of failure
support for multiple types of service
support for a variety of networks
distributed management of resources
cost effectiveness
easy addition of new hosts
accounting of resource usage

## Slide 19: The original text in SIGCOMM paper
1. Internet communication must continue despite loss of networks or gateways. （Survivability）
2. The Internet must support multiple types of communications service.
3. The Internet architecture must accommodate a variety of networks.
4. The Internet architecture must permit distributed management of its resources.
5. The Internet architecture must be cost effective.
6. The Internet architecture must permit host attachment with a low level of effort.
7. The resources used in the internet architecture must be accountable.

## Slide 20: Is there any priority order?
Yes. These goals are in order of importance, and an entirely different network architecture would result if the order were changed.
This network was designed to operate in a military context, which implied the possibility of a hostile environment, survivability was put as a first goal, and accountability as a last goal.

## Slide 21: Goal #1 Survivability
Network should continue to work, even if some devices fail, are compromised, etc.
In particular, this goal was interpreted to mean that if two entities are communicating over the Internet, and some failure causes the Internet to be temporarily disrupted and reconfigured to reconstitute the service, then the entities communicating should be able to continue without having to reestablish or reset the high level state of their conversation.

## Slide 22: State
To achieve this goal, the state information which describes the on-going conversation must be protected.
  Specific examples of state information would be the number of packets transmitted, the number of packets acknowledged, or the number of outstanding flow control permissions.
If the lower layers of the architecture lose this information, they will not be able to tell if data has been lost, and the application layer will have to cope with the loss of synchrony.

## Slide 23: Design options
Network should continue to work, even if some devices fail, are compromised, etc.
Two Options
Replication
  Keep state at multiple places in the network, recover when nodes crash
Fate-sharing
  Acceptable to lose state information for some entity if the entity itself is lost
Why fate-sharing
  Can support arbitrarily complex failure scenarios
  Engineering is easier

## Slide 24: Replication
In some network architectures, this state is stored in the intermediate packet switching nodes of the network.
  In this case, to protect the information from loss, it must replicated.
  Because of the distributed nature of the replication, algorithms to ensure robust replication are themselves difficult to build, and few networks with distributed state information provide any sort of protection against failure.

## Slide 25: Fate-sharing
The alternative, which this architecture chose, is to take this information and gather it at the endpoint of the net, at the entity which is utilizing the service of the network.
  this approach is called to reliability "fate-sharing."
it is acceptable to lose the state information associated with an entity if, at the same time, the entity itself is lost.
  Specifically, information about transport level synchronization is stored in the host which is attached to the net and using its communication service.

## Slide 26: Benefits
First, fate-sharing protects against any number of intermediate failures, whereas replication can only protect against a certain number (less than the number of replicated copies).
Second, fate-sharing is much easier to engineer than replication.

## Slide 27: Two design consequences
Stateless core
  First, the intermediate packet switching nodes, or gateways, must not have any essential state information about on-going connections. Instead, they are stateless packet switches, a class of network design sometimes called a "datagram" network.
Stateful edge
  Secondly, rather more trust is placed in the host machine than in an architecture where the network ensures the reliable delivery of data.

## Slide 28
Should we have states in the core?
Read More on e2e and fate-sharing http://mercury.lcs.mit.edu/~jnc/tech/end_end.html

## Slide 29: Goal #2: Heterogeneous Services
TCP/IP designed as a monolithic transport
  TCP for flow control, reliable delivery
  IP for forwarding
Became clear that not every type of application would need reliable, in-order delivery
  Example: Voice and video over networks
  Example: DNS
  Why don’t these applications require reliable, in-order delivery?
  Narrow waist: allowed proliferation of transport protocols

## Slide 30: Topic: Voice and Video over Networks
Loss in “Anchor” Frame (I-Frame)
Propagates to “Dependent” Frames (P and B-Frames)
Deadlines: Timeliness more important than 100% reliability.
Propagation of errors: Some losses more devastating than others

## Slide 31: Goal #3: Heterogeneous Networks
Build minimal functionality into the network
  No need to re-engineering for each type of network
“Best effort” service model.
  Lost packets
  Out-of-order packets
  No quality guarantees
  No information about failures, performance, etc.
Tradeoff: Network management more difficult

## Slide 32: Goal #4: Distributed Management
Addressing (ARIN, RIPE, APNIC, etc.)
  Though this was recently threatened.
Naming (DNS)
Routing (BGP)
Many examples:
No single entity in charge. Allows for organic growth, scalable management.
Tradeoff: No one party has visibility/control.

## Slide 33: No Owner, No Responsible Party
Hard to figure out who/what’s causing a problem
Worse yet, local actions have global effects…
“Some of the most significant problems with the Internet today relate to lack of sufficient tools for distributed management, especially in the area of routing.”

## Slide 34
Local Actions, Global Consequences
“…a glitch at a small ISP… triggered a major outage in Internet access across the country. The problem started when MAI Network Services...passed bad router information from one of its customers onto Sprint.” -- news.com, April 25, 1997
UUNet
Florida Internet
Barn
Sprint

## Slide 35: Goal #5: Cost Effectiveness
Packet headers introduce high overhead
End-to-end retransmission of lost packets
  Potentially wasteful of bandwidth by placing burden on the edges of the network
Arguably a good tradeoff. Current trends are to exploit redundancy even more.

## Slide 36: Goal #6: Ease of Attachment
IP is “plug and play” Anything with a working IP stack can connect to the Internet (hourglass model)
A huge success!
  Lesson: Lower the barrier to innovation/entry and people will get creative (e.g., Cerf and Kahn probably did not think about IP stacks on phones, sensors, etc.)
But….
Tradeoff: Burden on end systems/programmers.

## Slide 37: Goal #7: Accountability
Note: Accountability mentioned in early papers on TCP/IP, but not prioritized
Datagram networks make accounting tricky.
  The phone network has had an easier time figuring out billing
  Payments/billing on the Internet is much less precise
Tradeoff: Broken payment models and incentives.

## Slide 38: What’s Missing?
Security
Availability
Accountability (the other kind)
Support for disconnected/intermittent operation
Mobility
Scaling
…

## Slide 39: （1）可扩展性问题
一方面，随着用户数量和应用需求的不断增加，网络 流量增加的速度已远远超过摩尔定律与路由器性能提升的速度，这要求 IP 网络 基础设施每 2 年左右需要全面升级一次，导致运营商不断进行被动扩容，并为之 付出了大量成本。
另一方面，IPv4 地址枯竭且可扩展性差，骨干路由器的路由表急剧膨胀（全球路由表条目已经超过了 3087 万条），路由表条目的快速增长大大降低了路由查找性能，增加了路由器的系统开销，而在现有互联网体系结构中，只能通过不断地增加硬件设备性能来缓解该问题，尚未找到根本性的解决方案。

## Slide 40: （2）安全性问题
由于互 联网最初设计的主要目标是实现鲁棒性互联和资源共享，并未充分考虑到网络的 安全需求，虽然通过“打补丁”的方式在互联网中部署防火墙或陆续有 IPSec、 SSL/TLS、DNSSec、RADIUS 等技术被提出以加强网络安全性，但整个互联网 的安全保障仍处于被动应对的状态。
随着应用的增多，漏洞也在不断增多，包括恶意软件、分布式拒绝服务（DDoS）攻击、钓鱼软件、应用程序漏洞等安全威胁。
网络的安全性问题始终缺乏系统化、内生化的网络 安全体系。

## Slide 41: （3）可管可控性与服务质量保障问题
互联网采取了“尽力而为”的 服务机制，网络本身缺乏感知和测量功能。
同时 TCP/IP 网络采用分布式架构， 由端系统负责复杂的网络功能，即遵循将服务连接的维护管理工作交由终端完成 的设计原则，缺乏对网络资源的全局控制与管理，也没有真正有效的控制与资源 调度手段，如流量工程、操作维护、故障检测、容灾抗毁、资源管理功能以及业 务差异化等，越来越无法满足未来新型网络应用的需求。
随着网络规模越来越大， 如何实现网络系统的高效管控、自诊断、自恢复也成为亟需解决的关键难题。

## Slide 42: （4）移动性问题
早期互联网主要为以计算机为代表的具有一定处理能力 的固定终端提供数据交换服务。
目前，随着便携式移动设备和物联网、泛在网的 出现，互联网的终端形态发生了很大变化，突出表现为终端的移动性显著增加， 数据传输路径频繁变换
传统 TCP/IP 网络身份地址双重语义的设计规则不利于频繁的切换服务，无法保证低时延、不丢包的会话场景，尤其是对于高速移动的 车辆等服务对象，严重破坏了上层应用服务的连续性，甚至难以保证传统意义上 的端到端传输。

## Slide 43: （5）高效服务分发问题
过去十年推动互联网发展的主要趋势就是服务的多样性
视频服务如 UHD（超高清）、4K/8K 视频业务正在不断演进，导致视频服务面临着电视使用率不断减少、联网设备使用率和流传输不断增加的现状。
因此面对大量的服务需求，现有网络面临的一项重要挑 战就是如何实现高效的服务分发能力。

## Slide 44
The original design of the Internet emerged almost 30 years ago, a time that predates both the personal computer and local area networks.
Fiber optics had yet to emerge from the lab, the fastest cross-country circuit commercially available was about 50 kb/s
text was the only common user interface modality, and computing had not begun to reach the masses.

## Slide 45: （6）绿色与节能问题
传统互联网设计并未考虑能耗问题
互联网设备芯片容量与速度的提升，意味着更高的工作频率和复杂的加 工工艺，直接导致芯片耗电量的增大，从而增加了设备的功耗。
思科公司的分析报告显示，一些高端路由器能耗 甚至已高达兆瓦级。预测显示，全球互联网数据中心的用电功率可能达 300 亿瓦 特，相当于 30 个核电站的供电功率

## Slide 46: 改变互联网
随着网络规模持续扩大、用户数量不断增长、新型互联网业务层出不穷，传统 IP网络架构面临上述挑战
在此背景下，为了应对传统互联网体系结构逐渐暴露出的这些问题，世界各国已经实施了多项未来网络相关的研 究项目，提出了“演进型”和“革命型”两大类的技术路线和解决思路

## Slide 47: 路线之争
One Debate
“革命型” 、“演进型”
“clean slate” and “evolutionary”
Should researchers focus on designing new network architectures or improving the current Internet?

## Slide 48: “演进型”技术路线
主张在现有互联网网络体系架构下进行“补 丁式”的修补，即基于现有的 TCP/IP 协议栈，
  （1）提出新的组网技术，改变现 有网络形态，包括对网络设备或拓扑进行改造；
  （2）对已有的网络通信协议进行升级；
  （3）在现有网络中应用如人工智能、区块链、大数据等新技术手段。
从而暂时解决现网中日益暴露的各种问题，使得现有网络架构仍然能够在一定程 度上适应新的发展需求。

## Slide 49: “革命型”技术路线
认为任何技术体系都有它的生命周期，经过若干年就 可能发生较大的革新，IP 网络体系结构也不例外。
  由于 IP 网络体系结构在设计 的时候并没有充分考虑到当前网络应用的复杂性，因此“革命型”技术路线主张采取“Clean Slate”（从头再来）的策略，即在不受现有互联网约束的基础上探 讨新的网络体系结构，重新设计网络通信协议，并将其定义为未来网络体系架构。
目标是为了从根本上克服传统互联网体系结构在可扩展性、安全性、可管可控与 QoS 保障、移动性、服务分发以及绿色节能等方面的问题，更好地适应未来发展 需要，实现网络的可持续发展。

## Slide 50: 争论
虽然业界提出了“演进型”与“革命型”两大技术路线以解决当前网络面临 的问题，但是关于这两种技术路线的争议却很大，它们各有各的缺陷。
  “演进型” 技术路线会使得原本简洁的网络结构变得日益复杂和臃肿；
  而“革命型”技术路 线会减慢实际部署的步伐。

## Slide 51: 谢谢